Technical Summary

An environmental survey of the seabed surrounding the Central Azeri Platform was conducted by Akvamiljø Caspian (AmC) from 27-28 July 2010.

Sampling was conducted from the vessel Svetlomor 2 by personnel from AmC, the Ministry of Ecology and Natural Resources (MENR) and SOCAR. Sediment samples for physical and chemical analysis consisted of 2 replicates, while 3 replicates were taken for biological analyses. Analyses were carried out at AmC Caspian Environmental Laboratory.

Sediments around Central Azeri were very poorly sorted, the majority being a mixture of sand and gravel.  At many stations, the two replicates were substantially different, indicating patchiness of physical characteristics on a small spatial scale (metres).

LAO was detected at 7 stations in 2010. There was little evidence of change at the majority of stations, and the overall area within which LAO was observed remains very similar to that observed in previous surveys. In general the hydrocarbon concentrations were low or very low and UCM and NPD content were indicative of weathered material being present throughout the survey area.

For the majority of trace metals the data show no clear trends or gradients which could be associated with platform activities. Three elements – barium, cadmium, and lead – exhibited very similar concentration patterns.  These were the only elements which indicated a ‘footprint’ which was spatially related to the platform location.  A similar association was evident in the 2008 data.

The macrobenthic community was numerically dominated by amphipods which were also the most taxonomically rich group. There was a general tendency towards lower species richness and abundance at stations to the north of, and immediately to the south of, the platform, as was also noted in 2008.

The 2010 data for sediment composition, chemistry and macrobenthic biology suggest that there is an area immediately around the platform in which some degree of sediment alteration is present, and where there is a slightly lower macrobenthic community biomass and diversity relative to more distant stations.  However, there are no stations which could be considered biologically impoverished compared to previous surveys.

Glossary of terms

| Anthropogenic | Resulting from human activities |
| --- | --- |
| Aromatic hydrocarbon | Hydrocarbon with a molecular structure containing at least one benzene ring |
| Benthic | On or in the surface layers of the seabed |
| Bioavailable | Present in the environment in a form which can be taken up by plants or animals |
| Biogenic | Produced by the metabolic processes of living organisms |
| Biomass | The Weight of living material. Used as a measure per unit area or volume. |
| Classification | A mathematical procedure for categorising communities/locations where those with a similar composition are grouped together in subsets. |
| CVAF | Cold Vapour Atomic Fluorescence |
| Crustaceans | A group of animals including barnacles, copepods, amphipods, shrimps, crabs, lobsters |
| DCA | Detrended Correspondence Analysis, a method of statistical ordination |
| Dissolved oxygen | The amount of oxygen dissolved in the water column |
| Duplicate | One of two replicates. Often applied to laboratory replication – ie splitting one field sample into two portions for analysis, which gives an estimate of analytical variation |
| Gradient | A unidirectional trend in any measurement |
| GC-FID | Gas Chromatography - flame ionization detector |
| GC-MS | Gas chromatography-mass spectrometry |
| GFAAS | Graphite furnace atomic absorption spectroscopy |
| Heavy metals | A group of elements each of which is a metal with a specific density greater than 5.25 |
| Hydrocarbon | Organic compound composed of carbon and hydrogen atoms |
| ICP-OES | Inductively Coupled Plasma - Optical Emission Spectrometers |
| Macrofauna | Larger organisms; usually defined as those retained on a 0.5 mm sieve |
| MDS | Multidimensional Scaling, a method of statistical ordination |
| Mean particle size | Average sediment particle size, a measure of central tendency |
| Median diameter | A measure of central tendency – the particle diameter where the 50% frequency line intersects the cumulative frequency curve |
| NIO | National Institute of Oceanography |
| NPD | A collective term for the aromatic hydrocarbons: naphthalenes, phenanthrenes, and dibenzothiophenes. See ‘Chemical Terminology’ below. |
| Naphthalene | Two-ring aromatic hydrocarbon |
| Organic content | The weight of material removed by combustion of sediment at 600 °C (after removal of carbonate) |
| PAH | Polynuclear aromatic hydrocarbon. See ‘Chemical Terminology’ below. |
| PSA | Particle size analysis – the classification of sediment particle composition |
| Phenanthrene | Three-ring aromatic hydrocarbon |
| Phi grade scale (ø) | A logarithmic transformation of the Udden grade scale of sediment particle size categories based on the negative log (base 2) of the particle diameter |
| Polynuclear | Any chemical compound consisting of three or more linked rings of atoms |
| Pyrolytic | Derived from combustion sources |
| Replicate | Subunit of a sample: a sample consists of a number of replicates |
| Sample | A sample is a group of units (replicates) selected, usually at random, from a larger group (the population). By studying the sample it is hoped to draw valid conclusions about the population. |
| Station | A location within a study area where samples are or were collected |

Biological terminology

#### Abundance

The number of individual organisms in a population or community, combining “intensity” (density within inhabited areas) and ‘prevalence’ (number and size of inhabited areas).  Abundance is often used as an indication of the ability of the environment to support a healthy ecosystem.  Very low abundance can be the consequence of natural factors, but can also arise as a result of anthropogenic disturbance.  Very high abundance can also be an indicator of disturbance, especially if associated with low diversity and the dominance of the community by opportunistic species.

#### Evenness

A measure of the variability in abundance between species in a community.  High values of evenness mean that most species are present in similar numbers; low evenness indicates that the community is numerically dominated by only a few of the species present.

#### Richness

The number of species present in a sample or community.  A reduction in richness is often an indication of anthropogenic disturbance; a subsequent increase in richness is often interpreted as evidence of recovery from impact.

#### Diversity

Diversity is a measure that combines richness and evenness.  A community with many species is more diverse than one with few species.  Similarly, a community in which all species are of similar abundance is more diverse than one that is dominated by a few species.  The diversity statistic is essentially a statistical estimate of the probability that an individual chosen at random will belong to species x.  Since diversity reflects the combination of two properties, however, some caution should be observed when using the statistic as a basis for comparison between sampling locations.

#### Dominant Species

Species which make up a large proportion of the community biomass or numbers.

Chemical terminology

#### NPD

Low molecular weight PAHs – naphthalenes, phenanthrenes, and dibenzothiophenes.  These are more soluble and often more rapidly biologically active than higher molecular weight compounds.

#### EPA 16

A suite of 16 PAHs identified by the US Environmental Protection Agency as priority compounds with respect to environmental risk.

#### UCM

Unresolved complex mixture.  The term refers to those hydrocarbon compounds typically represented by a bell-shaped ‘hump’ in GC chromatograms.  The shape of the hump is often characteristic for specific types of industrial contamination, but the discrimination of individual compounds within the hump is rarely possible.

UCM compounds, which are found extensively in crude oil and its products, are very stable in the environment and therefore can be found in sediment even after substantial weathering and biodegradation of original hydrocarbon input (Farrington et al, 1977).

#### PAH

Polynuclear aromatic hydrocarbons and their alkyl homologues have been found in a wide range of marine sediments (Laflamme & Hites, 1978).  The major source of these compounds is thought to be anthropogenic combustion although other combustion sources such as forest fires probably make a significant contribution (Youngblood & Blumer, 1975).  Once released into the atmosphere the PAHs may be carried long distances adsorbed to particulate material such as soot and flyash (Windsor & Hites, 1979).  Upon deposition in the environment the particulate may undergo further transport for example by rivers or ocean currents before final deposition in the sediment.

Petroleum is another potential source of aromatic hydrocarbons in the environment, particularly from point sources such as operational discharges or from oil spills.  Petroleum is rich in aromatic hydrocarbons, particularly 1-3 ring compounds (benzenes, naphthalenes, and phenanthrenes), the levels of 4-6 ring compounds being relatively low.  In addition, significant concentrations of dibenzothiophenes are normally present.  The relative proportion of these compounds will vary between different crude oils (and refined products).

The distributions of PAH in sediments will be determined by their source, solubility, and relative rates of biodegradation.  Because of their low solubility and hydrophobic nature, PAH tend to be adsorbed by the inorganic and organic particulate matter in the water column, which gradually settles out.  Once deposited in the sediment PAHs are less susceptible to photochemical and biological oxidation and may accumulate to relatively high concentrations.

PAHs are often more toxic than straight-chain hydrocarbons, and have a wider range of potential biological effects.  PAHs have been shown to interfere with a variety of biochemical processes, with possible implications for chronic and reproductive damage.

Other terms

#### Standard deviation

A measure of the variability of data around the mean value.  Strictly, this should be applied only where it is known that the data have been collected from a single ‘population’.

#### Coefficient of variation

Also known as ‘relative standard deviation’, this expresses the standard deviation as a percent of the mean, and thus provides a simple way to compare variability between data of similar type.  For instance, calculating the coefficients of variation for trace metal concentrations in sediments allows a comparison of variability for metals (such as iron and mercury) which differ substantially in their typical concentrations.

Contents List

Section	Page

1	Introduction	1-1

2	Fieldwork and Analytical Programme	2-1

3	Seabed Characteristics	3-1

4	Sediment Hydrocarbons	4-1

5	Trace Metals in Sediments	5-1

6	Macrofaunal Biology	6-1

7	Water Column 	7-1

8	Discussion & Recommendations	8-1

Appendices

1 Survey Log Sheets

2 Analytical Methods

3 PSA Histograms

4 GC Chromatograms

5 PAH Data

6 2010 Replicate Macrobenthic Data

Central Azeri

Environmental Survey

July 2010

AmC Project 10502

| Report number 10502-R2 | Author, Company: Brian Roddie | Date: 17 January 2012 |
| --- | --- | --- |
| Number of pages: 83 | Work participant(s): AmC Caspian Environmental Laboratory | Client: BP Contact person: Faig Askerov, Afag Abbasova |
| ISBN: N/A | Distribution restriction: Confidential | Open from (date): |
| Scope: Provide information on the sediment chemistry, macrobenthic fauna and physical characteristics and compare the data collected with previous data sets from the 2001 baseline survey. If changes to the sediment chemistry, macrobenthic fauna and physical characteristics were identified, assess if they are attributed to natural or anthropogenic stresses. |
| Key-words: ACG Contract Area, Central Azeri, Offshore, Seabed, Water, Environmental Monitoring |

No part of this document may be reproduced in any form without permission in writing by Akvamiljø Caspian -AmC ©.

| Project leader |  |  |  | AmC Managing Director |
| --- | --- | --- | --- | --- |
| James McNee |  |  |  | Nils Skeby |

Akvamiljø Caspian

Shikh Settlement

Salyan Highway

Sabail District

Baku AZ1 800

Azerbaijan

for further information contact

James McNee

tel		+994 12 4974775 / 4974776

fax		+994 12 4974002

e-mail	james.mcnee@amc.az