# Fieldwork and analytical programme

## Survey execution and sample collection

The survey was conducted on the 27th and 28th of July 2010, the survey log is provided in appendix 1. The survey vessel was the Svetlomor II.  The following personnel participated in the survey:

- James McNee, AmC Senior Consultant

- Ilgar Guliyev, AmC Senior Scientist

- Mustafa Gafarov, AmC Scientist

- Irada Israfilova, AmC Scientist

- Konul Guliyeva, AmC Scientist

- Faruhk Fursi, AmC Technician

- Kamran Ahmedov, AmC Technician

- Andrey Fomin, AmC Technician

- Valeh Karimov MENR Scientist

- Hikmet Zeynalov SOCAR Scientist

The 2010 survey planned to sample the same station positions as 2008. However, during the survey the position of stations 6, 11, 14, 15, 18 and 21 were moved from the planned location to allow safe clearance of seabed assets. Figure 2.1 presents an overlay of the 2006, 2008 and 2010 stations. In eight cases, station locations have changed sufficiently to make direct comparisons of individual stations between surveys impracticable; however, the overall station layout has been sufficiently well preserved to permit a comparison of spatial patterns between surveys. The distance from the planned original positions are included in table 2.1 below.  Station 10W1 is a water sampling station which was added due to bad weather access restrictions to the originally planned position.

Figure 2.1 2006, 2008 and 2010 Survey Sample Stations Overlay

## Sediment Samples

A standard survey was carried out, using a 0.1 m2 van Veen grab to collect samples from the top 10-15 cm of sediment.  Two replicate samples were collected at each station for physical (particle size) and chemical analysis and three replicate samples were collected at selected stations for biological analysis (see table 2.2).  Biological samples were washed on a 0.5 mm sieve, and all material retained was preserved in 4% formaldehyde solution.  Subsamples for physical and chemical analysis were placed in appropriate labelled containers and stored in a freezer on the Svetlomor II, then transferred to freezer storage at AmC’s Caspian Environmental Laboratory at the end of the survey. The co-ordinates for the sediment sample stations are listed in Table 2.1.

## Sampling & Analytical Programme

Details of the analytical methods are provided in Appendix 2 of this report.  The analytical work was conducted at AmC Caspian Environmental Laboratory. All sampling and laboratory work was carried out in accordance with AmC’s quality system.

Table 2.1	Co-ordinates of Seabed Stations

|  |  |  |  | Positional Change 2006-2008 | Positional change 2008-2010 |
| --- | --- | --- | --- | --- | --- |
| Station | Easting | Northing | Depth | Distance | Direction | Distance | Direction |
| CA 1001 | 529628 | 4434052 | 131 |  |  |  |  |
| CA 1002 | 530628 | 4434052 | 134 |  |  |  |  |
| CA 1003 | 529878 | 4433619 | 127 |  |  |  |  |
| CA 1004 | 530196 | 4433652 | 128 | 48 | E |  |  |
| CA 1005 | 530432 | 4433705 | 130 | 102 | NE |  |  |
| CA 1006 | 529961 | 4433447 | 127 |  |  | 59 | NNW |
| CA 1008 | 530522 | 4433471 | 129 | 71 | NNE |  |  |
| CA 1009 | 530317 | 4433298 | 128 |  |  |  |  |
| CA 1010 | 529128 | 4433186 | 140 |  |  |  |  |
| CA 1011 | 529544 | 4433157 | 139 | 66 | W | 51 | SSW |
| CA 1012 | 530775 | 4433076 | 131 | 122 | SE |  |  |
| CA 1013 | 531128 | 4433186 | 133 |  |  |  |  |
| CA 1014 | 529762 | 4432896 | 135 | 31 | SW | 42 | SE |
| CA 1015 | 530229 | 4432924 | 133 |  |  | 50 | W |
| CA 1016 | 530487 | 4432986 | 135 | 23 | NW |  |  |
| CA 1017 | 529878 | 4432753 | 135 |  |  |  |  |
| CA 1018 | 530178 | 4432638 | 138 | 105 | N | 32 | ESE |
| CA 1019 | 530356 | 4432786 | 136 | 40 | NW |  |  |
| CA 1020 | 529628 | 4432320 | 146 |  |  |  |  |
| CA 1021 | 530630 | 4432442 | 159 | 57 | NE | 35 | SW |
| CA 1022 | 529353 | 4433441 | 135 | Added |  |  |  |
| CA 10W1 | 529801 | 4433736 |  |  |  |  | Water station added |

### Analytical Programme

The analytical programme for the sediment samples is presented in table 2.2 below.  All twenty-one stations were selected for chemical and biological work-up of samples.

Table 2.2	Sediment Sampling and Analysis Plan

| Station | Physical and chemical analyses | Biological analysis |
| --- | --- | --- |
|  | HC1 | HM2 | PSA3 | Phenols4 | Taxonomy, abundance, and biomass |
| CA 1001 | 2 | 2 | 2 | 2 | 3 |
| CA 1002 | 2 | 2 | 2 | 2 | 3 |
| CA 1003 | 2 | 2 | 2 | 2 | 3 |
| CA 1004 | 2 | 2 | 2 | 2 | 3 |
| CA 1005 | 2 | 2 | 2 | 2 | 3 |
| CA 1006 | 2 | 2 | 2 | 2 | 3 |
| CA 1008 | 2 | 2 | 2 | 2 | 3 |
| CA 1009 | 2 | 2 | 2 | 2 | 3 |
| CA 1010 | 2 | 2 | 2 | 2 | 3 |
| CA 1011 | 2 | 2 | 2 | 2 | 3 |
| CA 1012 | 2 | 2 | 2 | 2 | 3 |
| CA 1013 | 2 | 2 | 2 | 2 | 3 |
| CA 1014 | 2 | 2 | 2 | 2 | 3 |
| CA 1015 | 2 | 2 | 2 | 2 | 3 |
| CA 1016 | 2 | 2 | 2 | 2 | 3 |
| CA 1017 | 2 | 2 | 2 | 2 | 3 |
| CA 1018 | 2 | 2 | 2 | 2 | 3 |
| CA 1019 | 2 | 2 | 2 | 2 | 3 |
| CA 1020 | 2 | 2 | 2 | 2 | 3 |
| CA 1021 | 2 | 2 | 2 | 2 | 3 |
| CA 1022 | 2 | 2 | 2 | 2 | 3 |

1	HC = Hydrocarbon analysis: THC by GC-FID, 2-6 ring PAH by GC-MS and phenols by spectrophotometry (Merck Spectroquant method)

2	HM = Heavy metal analysis: All metals except Hg analysed by ICP-OES, Hg analysed CVAFS

3	PSA = Particle size analysis: Grain size distribution, total organic matter (TOM), carbonate (CO3)

4	Phenols will be measured by spectrophotometry (Merck Spectroquant method)

In compliance with the scope of the 2008 survey, 5 water sampling stations were included in the 2010 survey. The water sample positions are given in table 2 and are presented graphically in figure 2.1 above.

Two samples were taken at each station, one from the surface (0-3m) and one from below the thermocline. The position of the thermocline was established by the use of a CTD sensor. The water sample analysis plan is given in table 2.4.

Table 2.3 Water sample locations

| Station | Easting | Northing |
| --- | --- | --- |
| CA 1008 | 530522 | 4433471 |
| CA 1010 | 529128 | 4433186 |
| CA 1012 | 530775 | 4433076 |
| CA 1020 | 529628 | 4432320 |
| CA 10W1 | 529801 | 4433736 |

Table 2.4 Water Sample Analysis Plan

| Determinand | Method | Method of sampling and preservation for transport to laboratory |
| --- | --- | --- |
| Temperature | pH meter | N/A – analyses conducted immediately |
| Salinity | Multimeter |  |
| Dissolved oxygen | DO meter |  |
| Turbidity | Turbidimeter |  |
| pH | pH meter |  |
| Total suspended solids (TSS) | EN 872 | Water is filtered through pre-weighed membrane filter. Filter is placed in labelled plastic Petri dish, dish is sealed and frozen. |
| Total nitrogen, total phosphorus, nitrate, nitrite, ammonia, phosphate, silicate, BOD & COD | Grasshoff et al | Water is poured into two (duplicate) sterile 1-litre plastic bottles, then frozen. 2 litres of water is sufficient for all nutrient analyses. |
| THC | GC-FID | Water is poured into 2 x 1litre, DCM-cleaned, amber glass bottle, then refrigerated |
| PAH | GC-MS |  |
| Phenols | Merck Spectroquant |  |
| Metals (Fe, Cd, Co, Cu, Ni, Pb, Zn) | ICP-MS | Water is poured from NIOS bottle into 0.5-L acid-washed, plastic bottles, then refrigerated |

# Text boxes

2010

2008

+	2006