# Metals in Sediments

## Results

Metal concentrations at each East Azeri sample station were determined from 2 replicate sediment samples. Replicate values are given in Table 5.1, which also indicates the minimum, maximum, median and average values together with the coefficient of variation.  To assist visualisation of variation in values, concentrations which differ from the median by less than 25% are highlighted in yellow, and orange highlighting is used to indicate coefficients of variation larger than would be expected to arise from sampling and analytical variation. Table 5.2 gives the range, coefficient of variation and mean for each element recorded on previous East Azeri surveys.

Table 5.1 Replicate Metal Concentrations (μg.g-1) East Azeri Survey 2010

| Station | Rep | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EAP 1001 | 1 | 9.8 | 2776 | 3,234 | 0.35 | 44.9 | 26.4 | 0.02 | 18133 | 384 | 10.4 | 53.0 |
|  | 2 | 9.9 | 3782 | 5,030 | 0.65 | 32.5 | 29.3 | 0.04 | 14252 | 281 | 12.1 | 47.2 |
| EAP 1002 | 1 | 15.0 | 3159 | 3,550 | 0.43 | 36.1 | 24.4 | 0.03 | 18706 | 637 | 12.7 | 50.5 |
|  | 2 | 8.5 | 2596 | 3,342 | 0.43 | 24.7 | 18.2 | 0.03 | 11868 | 267 | 9.4 | 34.9 |
| EAP 1003 | 1 | 11.2 | 4033 | 5,775 | 0.56 | 37.1 | 32.1 | 0.05 | 16212 | 335 | 32.1 | 54.4 |
|  | 2 | 14.2 | 1587 | 1,772 | 0.01 | 46.4 | 25.6 | 0.02 | 21475 | 494 | 10.4 | 55.7 |
| EAP 1004 | 1 | 12.8 | 4378 | 5,114 | 0.61 | 34.3 | 26.5 | 0.04 | 15948 | 293 | 11.8 | 44.5 |
|  | 2 | 11.9 | 6174 | 8,436 | 0.76 | 43.1 | 31.0 | 0.02 | 19700 | 379 | 11.4 | 53.7 |
| EAP 1005 | 1 | 10.0 | 3458 | 5,450 | 0.56 | 37.9 | 26.3 | 0.03 | 16103 | 324 | 10.1 | 47.8 |
|  | 2 | 9.8 | 6622 | 9,683 | 1.04 | 43.4 | 29.3 | 0.02 | 17881 | 388 | 11.4 | 51.5 |
| EAP 1006 | 1 | 13.9 | 819 | 1,024 | 0.16 | 39.2 | 22.0 | 0.02 | 20891 | 362 | 9.6 | 47.5 |
|  | 2 | 9.4 | 2760 | 4,229 | 0.57 | 23.5 | 15.3 | 0.03 | 11761 | 286 | 8.6 | 30.2 |
| EAP 1007 | 1 | 12.6 | 1498 | 2,194 | 0.28 | 47.8 | 27.1 | 0.02 | 22489 | 459 | 10.6 | 54.3 |
|  | 2 | 11.7 | 2103 | 2,767 | 0.38 | 40.8 | 23.0 | 0.03 | 18871 | 430 | 9.6 | 46.7 |
| EAP 1008 | 1 | 17.2 | 923 | 1,310 | 0.22 | 56.9 | 23.1 | 0.02 | 28029 | 531 | 11.4 | 63.6 |
|  | 2 | 16.0 | 3074 | 3,992 | 0.48 | 53.1 | 22.4 | 0.02 | 27058 | 493 | 11.7 | 59.9 |
| EAP 1009 | 1 | 10.8 | 6127 | 8,759 | 0.97 | 44.5 | 28.7 | 0.02 | 20036 | 395 | 11.5 | 54.6 |
|  | 2 | 13.0 | 7272 | 10,932 | 1.36 | 41.1 | 31.2 | 0.03 | 18518 | 371 | 13.6 | 62.2 |
| EAP 1010 | 1 | 10.1 | 2947 | 3,567 | 0.55 | 26.7 | 17.4 | 0.03 | 12936 | 282 | 9.0 | 33.8 |
|  | 2 | 10.7 | 2895 | 3,782 | 0.55 | 39.4 | 23.5 | 0.03 | 18868 | 351 | 11.0 | 49.1 |
| EAP 1011 | 1 | 14.5 | 1841 | 2,675 | 0.57 | 35.8 | 29.6 | 0.03 | 16715 | 324 | 9.8 | 42.1 |
|  | 2 | 10.7 | 1670 | 2,791 | 0.41 | 44.0 | 34.7 | 0.03 | 18742 | 310 | 12.1 | 50.7 |
| EAP 1012 | 1 | 13.6 | 4586 | 7,012 | 0.85 | 52.3 | 31.8 | 0.02 | 23077 | 436 | 12.0 | 57.0 |
|  | 2 | 15.8 | 845 | 1,283 | 0.14 | 51.0 | 22.0 | 0.02 | 25331 | 448 | 10.6 | 56.2 |
| EAP 1013 | 1 | 12.3 | 4800 | 6,486 | 0.90 | 44.0 | 22.8 | 0.02 | 18394 | 347 | 12.1 | 50.1 |
|  | 2 | 9.7 | 2774 | 4,083 | 0.59 | 31.6 | 19.8 | 0.02 | 14111 | 299 | 8.4 | 38.7 |

Table 5.1 (Continued)  Replicate Metal Concentrations (μg.g-1) East Azeri Survey 2010

| Station | Rep | As | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| EAP 1014 | 1 | 10.2 | 5720 | 8,602 | 0.99 | 41.0 | 24.9 | 0.03 | 18842 | 377 | 13.0 | 52.0 |
|  | 2 | 10.9 | 4960 | 7,029 | 0.86 | 42.6 | 22.7 | 0.03 | 18271 | 359 | 11.4 | 48.7 |
| EAP 1015 | 1 | 15.7 | 1549 | 1,974 | 0.29 | 52.4 | 31.7 | 0.03 | 24281 | 461 | 12.4 | 59.6 |
|  | 2 | 21.9 | 5401 | 7,304 | 1.11 | 31.9 | 18.8 | 0.02 | 17242 | 354 | 12.7 | 41.0 |
| EAP 1016 | 1 | 13.5 | 2449 | 2,496 | 0.48 | 39.3 | 22.5 | 0.04 | 17355 | 329 | 10.5 | 44.0 |
|  | 2 | 12.3 | 1042 | 2,053 | 0.25 | 44.4 | 27.4 | 0.05 | 18767 | 373 | 9.6 | 49.8 |
| EAP 1017 | 1 | 11.1 | 1109 | 1,148 | 0.23 | 44.3 | 22.0 | 0.03 | 20080 | 377 | 9.7 | 49.4 |
|  | 2 | 9.4 | 338 | 706 | 0.04 | 44.9 | 20.4 | 0.03 | 20645 | 400 | 9.4 | 50.2 |
| EAP 1018 | 1 | 8.9 | 5125 | 6,966 | 1.00 | 30.7 | 28.1 | 0.04 | 13187 | 337 | 11.1 | 39.6 |
|  | 2 | 7.4 | 5142 | 5,855 | 0.97 | 25.5 | 21.1 | 0.03 | 11472 | 274 | 9.1 | 32.6 |
| EAP 1019 | 1 | 11.5 | 1263 | 1,624 | 0.23 | 41.5 | 24.7 | 0.04 | 19149 | 372 | 10.5 | 48.9 |
|  | 2 | 12.5 | 1106 | 1,367 | 0.32 | 42.5 | 23.5 | 0.03 | 21256 | 404 | 10.4 | 51.0 |
| EAP 1020 | 1 | 12.7 | 1754 | 2,425 | 0.29 | 48.8 | 20.4 | 0.04 | 25717 | 393 | 10.7 | 51.1 |
|  | 2 | 10.6 | 3424 | 3,717 | 0.78 | 39.3 | 36.0 | 0.05 | 17022 | 358 | 11.2 | 50.3 |
| EAP 1021 | 1 | 14.6 | 4308 | 6,201 | 0.95 | 27.5 | 15.7 | 0.03 | 14179 | 313 | 8.3 | 31.8 |
|  | 2 | 18.3 | 5692 | 5,899 | 1.15 | 26.8 | 15.1 | 0.03 | 14877 | 443 | 9.1 | 30.4 |
| Min |  | 7.4 | 338 | 706 | 0.01 | 23.5 | 15.1 | 0.02 | 11472 | 267 | 8.3 | 30.2 |
| Max |  | 21.9 | 7272 | 10932 | 1.36 | 56.9 | 36.0 | 0.05 | 28029 | 637 | 32.1 | 63.6 |
| Median |  | 11.8 | 2921 | 3749 | 0.56 | 41.1 | 23.9 | 0.03 | 18612 | 372 | 10.7 | 50.0 |
| Average |  | 12.3 | 3235 | 4372 | 0.58 | 39.9 | 24.7 | 0.03 | 18534 | 377 | 11.2 | 48.1 |
| St Dev |  | 2.87 | 1854 | 2631 | 0.33 | 8.29 | 5.16 | 0.01 | 4014 | 76 | 3.55 | 8.50 |
| CV |  | 23% | 57% | 60% | 57% | 21% | 21% | 30% | 22% | 20% | 32% | 18% |

Table 5.2 Comparable Replicate Metal Range & Mean Concentrations μg.g-1 East Azeri 2002, 2006, 2008 & 2010

|  | Year | Min | Mean | Max | % CV |
| --- | --- | --- | --- | --- | --- |
|  | 2010 | 7.4 | 12.3 | 21.9 | 23 |
| As | 2008 | 3.1 | 7.9 | 20.7 | 47 |
|  | 2006 | 4.9 | 10.3 | 27.4 | 52 |
|  | 2002 | 2.1 | 4.4 | 9.7 | 42 |
|  | 2010 | 338 | 3235 | 7272 | 57 |
| Ba HNO3 | 2008 | 407 | 3,156 | 12,690 | 94 |
|  | 2006 | 244 | 4,985 | 19,800 | 98 |
|  | 2002 | 358 | 1,153 | 3,381 | 58 |
|  | 2010 | 706 | 4,372 | 10,932 | 60 |
| Ba Fusion | 2008 | 550 | 3,717 | 15,660 | 96 |
|  | 2006 | 536 | 6,256 | 22,200 | 91 |
|  | 2010 | 0.01 | 0.58 | 1.36 | 57 |
| Cd | 2008 | 0.18 | 0.29 | 0.64 | 36 |
|  | 2006 | 0.07 | 0.31 | 0.83 | 55 |
|  | 2002 | 0.14 | 0.17 | 0.2 | 10 |

Table 5.2 (Continued) Comparable Replicate Metal Range & Mean Concentrations μg.g-1 East Azeri 2002, 2006, 2008 & 2010

|  | Year | Min | Mean | Max | % CV |
| --- | --- | --- | --- | --- | --- |
|  | 2010 | 23.5 | 39.9 | 56.9 | 21 |
| Cr | 2008 | 29.2 | 49.6 | 67.4 | 19 |
|  | 2006 | 16.6 | 42.5 | 60.2 | 21 |
|  | 2002 | 33.9 | 47.7 | 70.4 | 20 |
|  | 2010 | 15.1 | 24.7 | 36 | 21 |
| Cu | 2008 | 22.3 | 30.1 | 39.5 | 15 |
|  | 2006 | 12.5 | 32.1 | 45.9 | 19 |
|  | 2002 | 20.2 | 26.2 | 37.2 | 13 |
|  | 2010 | 0.02 | 0.03 | 0.05 | 30 |
| Hg | 2008 | 0.016 | 0.03 | 0.054 | 36 |
|  | 2006 | 0.01 | 0.024 | 0.2 | 119 |
|  | 2010 | 11472 | 18534 | 28029 | 22 |
| Fe | 2008 | 14,200 | 23,468 | 32,300 | 20 |
|  | 2006 | 9,240 | 21,020 | 39,600 | 24 |
|  | 2002 | 14,376 | 20,713 | 30,173 | 21 |
|  | 2010 | 267 | 377 | 637 | 20 |
| Mn | 2008 | 285 | 468 | 695 | 18 |
|  | 2006 | 257 | 478 | 1,500 | 40 |
|  | 2002 | 287 | 406 | 613 | 19 |
|  | 2010 | 8.3 | 11.2 | 32.1 | 32 |
| Pb | 2008 | 7.5 | 10.8 | 13.8 | 15 |
|  | 2006 | 7.4 | 11.8 | 15.6 | 14 |
|  | 2002 | 9.2 | 23 | 35.6 | 26 |
|  | 2010 | 30.2 | 48.1 | 63.6 | 18 |
| Zn | 2008 | 34.5 | 55.1 | 82.1 | 15 |
|  | 2006 | 19.8 | 45.4 | 58.9 | 15 |
|  | 2002 | 31.1 | 45.6 | 61.9 | 16 |

Examination of the replicate data indicates that replicate agreement was generally good. The largest between-replicate differences were observed at stations 5, 6, 12, 13 and 15, and the differences were most marked for barium, cadmium and iron.

Arsenic

Arsenic concentrations ranged from 7.4 to 21.9μg.g-1 with median and average concentrations of 11.8 and 12.3μg.g-1 respectively and a coefficient of variation of 23%.  Table 5.3 presents these and the corresponding statistics for 2008 and 2006.  Median and average concentrations are slightly higher in 2010 than in previous surveys, but the maximum concentration observed is similar to 2008.  Variability between samples is lower in 2010 than in previous surveys, and this, together with the higher average concentrations, is reflected in Figure 5.1; in this figure, there are some similarities between 2010 and 2008, but it appears that while concentrations are lower in the NE sector of the survey area, the previous area of higher concentration extends in 2010 from the south of the platform to the north of the platform.  In 2010, the highest concentrations were observed at stations 8, 12, 15 and 21.  However, although some variation in the pattern of distribution of values is apparent, it is clear from Table 5.3 that there is little change in the overall levels over time.

Table 5.3  Summary statistics, arsenic concentrations 2006-2010

|  | 2006 | 2008 | 2010 |
| --- | --- | --- | --- |
| Min | 4.9 | 3.1 | 7.4 |
| Max | 27.4 | 20.7 | 21.9 |
| Median | 8.7 | 7.1 | 11.8 |
| Average | 10.3 | 7.9 | 12.3 |
| St Dev | 5.3 | 3.7 | 2.9 |
| CV | 52% | 47% | 23% |

Figure 5.1  Average arsenic concentrations, East Azeri 2008 and 2010

Barium

Analysis for total barium (fusion) was carried out to identify the extent of contamination from drilling discharges as barite in drilling fluids interferes with the determination of HNO3 extracted Ba.

The 2002 pre-drill survey recorded a maximum HNO3 extracted Ba concentration of 3,381μg.g-1 and analysis for total Ba Fusion did not commence until 2006. Figure 5.2 below gives the distribution plots for total and HNO3 extracted Ba indicating the 4,000 μg.g-1 contour.

Figure 5.2	Contour Plots Average Ba Concentrations East Azeri Survey 2008 and 2010

Table 5.4 presents summary statistics for both forms of barium for 2006, 2008 and 2010. Maximum concentrations have progressively declined, presumably reflecting the lower intensity of platform drilling compared to the predrill programme.  However, median and average concentrations of both forms are higher in 2010 than in 2008, whilst the coefficient of variation has reduced substantially. These changes are clearly reflected in Figure 5.2, which is consistent with a progressive ‘spread’ of previously deposited material, resulting in a reduction in concentration within the previous footprint, but an increase in the area within which concentrations are higher than the baseline maximum.

Table 5.4  Summary statistics, barium concentrations 2006-2010

|  | Ba HNO3 |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 244 | 407 | 338 |
| Max | 19800 | 12690 | 7272 |
| Median | 3205 | 2390 | 2921 |
| Average | 4985 | 3156 | 3235 |
| St Dev | 4910 | 2958 | 1854 |
| CV | 98% | 94% | 57% |

Table 5.4  (Continued) Summary statistics, barium concentrations 2006-2010

|  | Ba Fusion |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 536 | 550 | 706 |
| Max | 22200 | 15660 | 10932 |
| Median | 4145 | 2600 | 3749 |
| Average | 6256 | 3717 | 4372 |
| St Dev | 5680 | 3574 | 2631 |
| CV | 91% | 96% | 60% |

Cadmium

The most notable difference in cadmium concentrations between 2010 and previous surveys is that the maximum, median and average concentrations are more than two times higher (Table 5.5).  Whilst Figure 5.3 indicates a moderate level of consistency between surveys, with higher concentrations to the east of the survey area and at station 18 to the west, there is a trend in 2010 towards higher concentrations at all stations except those to the immediate west of the  platform, together with stations 16, 17 and 19 on the northern and eastern edges of the survey area.  The change in pattern for Cd closely matches the change in pattern noted above for Ba. However, the changes in absolute concentration in these two metals are quite different; barium concentrations did not show a corresponding increase between 2008 and 2010.

Table 5.5  Summary statistics, cadmium concentrations 2006-2008

|  | Cd |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 0.07 | 0.18 | 0.01 |
| Max | 0.83 | 0.64 | 1.36 |
| Median | 0.26 | 0.27 | 0.56 |
| Average | 0.31 | 0.29 | 0.58 |
| St Dev | 0.17 | 0.11 | 0.33 |
| CV | 55% | 36% | 57% |

Figure 5.3  Contour plots, average Cd concentrations 2008 and 2010

Chromium

Chromium concentrations ranged from 23.5 μg.g-1 to 56.9 μg.g-1, with median and average values of 41.1 and 39.9 μg.g-1 and a coefficient of variation of 21%.  Minimum, maximum, median and average values were lower than in 2008 but (with the exception of the minimum value) were very similar to 2006.  The coefficient of variation has remained constant at around 20% over all three surveys, and represents a degree of variability which is close to the limits of sampling and analytical uncertainty.

Figure 5.4 presents the spatial pattern of chromium concentrations in 2008 and 2010.  These both indicate a zone of higher concentration immediately to the west and south of the platform, but the 2010 contour plot reflects concentrations which are lower than in 2008 in all other directions.

Table 5.6  summary statistics, chromium concentrations 2006-2010

|  | Cr |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 16.6 | 29.2 | 23.5 |
| Max | 60.2 | 67.4 | 56.9 |
| Median | 44.1 | 50.6 | 41.1 |
| Average | 42.5 | 49.6 | 39.9 |
| St Dev | 8.8 | 9.3 | 8.3 |
| CV | 21% | 19% | 21% |

Figure 5.4  Contour plots, average chromium concentrations 2008 and 2010

Copper

Copper concentrations ranged from 15.1 to 36 μg.g-1, with median and average values of 23.9 and 24.7 μg.g-1 respectively, and a coefficient of variation of 21%. With the exception of the coefficient of variation (which was higher than in 2008 and similar to 2006), all summary parameters were lower in 2010 than in 2008 (Table 5.7).

A comparison of contour plots of concentration between 2008 and 2010 (Figure 5.5) illustrates a general reduction in concentration over the  survey area, and some changes in the pattern of distribution of values.  Whilst there remains some indication of a patch of higher concentration around stations 1, 4, 5, and 9,  higher concentrations were also observed at station 11, which in 2008 was within an area of lower concentration.  However, the very low coefficient of variation indicates that these patterns are of limited significance and largely represent natural variation.

Table 5.7 Summary statistics for copper, 2006-2010

|  | Cu |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 12.5 | 22.3 | 15.1 |
| Max | 45.9 | 39.5 | 36.0 |
| Median | 32.7 | 29.0 | 23.9 |
| Average | 32.1 | 30.1 | 24.7 |
| St Dev | 6.0 | 4.4 | 5.2 |
| CV | 19% | 15% | 21% |

Figure 5.5 Contour plots, average copper concentrations, 2008 and 2010

Mercury

Mercury concentrations ranged from 0.02 to 0.05μg.g-1, with a median and average value of 0.03μg.g-1 and a coefficient of variation of 30%.  All summary parameters were very similar to those observed in the 2008 data set (Table 5.8).

Figure 5.6 compares concentration contour plots for 2008 and 2010.  The pattern is very different between the two surveys; in 2008, distribution of values was very patchy, with scattered peaks of concentration (one of which centred on the platform), while in 2010 the pattern appeared more systematic, with the lowest concentrations located at the stations within a 250-500m radius of the platform.  The coefficient of variation is moderate, so some of this change might be due to chance; however, it could equally be (at least in part) attributable to the progressive spread of more homogenous material derived from cuttings deposited close to the platform.

Table 5.8 Summary statistics for mercury, 2006-2010

|  | Hg |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 0.01 | 0.02 | 0.02 |
| Max | 0.20 | 0.05 | 0.05 |
| Median | 0.02 | 0.03 | 0.03 |
| Average | 0.02 | 0.03 | 0.03 |
| St Dev | 0.03 | 0.01 | 0.01 |
| CV | 119% | 36% | 30% |

Figure 5.6 Contour plots, average mercury concentrations, 2008 and 2010

Iron

Iron concentrations ranged from 11,472 to 28,029 μg.g-1, with median and average values of 18,612 and 18,534 μg.g-1 and a coefficient of variation of 22%.  All summary parameters, with the exception of the coefficient of variation, were slightly lower in 2010 than in 2008 and 2006 (Table 5.9).  Figure 5.7 indicates that there remains a patch of higher concentration around stations 8 and 12, to the immediate south/southwest of the platform, but there is evidence of a reduction in concentration around stations 5 and 10 (to the NE of the platform) and also at station 21 at the SE limit of the survey area.

Table 5.9 Summary statistics for iron, 2006-2010

|  | Fe |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 9240 | 14200 | 11472 |
| Max | 39600 | 32300 | 28029 |
| Median | 20750 | 24750 | 18612 |
| Average | 21020 | 23468 | 18534 |
| St Dev | 5148 | 4618 | 4014 |
| CV | 24% | 20% | 22% |

Figure 5.7 Contour plots, average iron concentrations, 2008 and 2010

Manganese

Manganese concentrations ranged from 267 to 637 μg.g-1, with median and average values of 372 and 377 μg.g-1 and a coefficient of variation of 20%.  The 2010 summary statistics were  lower in magnitude than the 2008 and 2006 data (Table 5.10).

Figure 5.8 indicates that the zone of highest concentration remains centred on stations 8 and 12, but that there has, between 2008 and 2010, been a marked reduction in concentration in the east and south of the survey area.  The apparent change in pattern is similar to that illustrated in Figure 5.7 for iron.

Table 5.10 Summary statistics for manganese, 2006-2010

|  | Mn |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 257 | 285 | 267 |
| Max | 1500 | 695 | 637 |
| Median | 432 | 476 | 372 |
| Average | 478 | 468 | 377 |
| St Dev | 192 | 86 | 76 |
| CV | 40% | 18% | 20% |

Figure 5.8 Contour plots, average manganese concentrations, 2008 and 2010

Lead

Lead concentrations ranged from 8.3 to 32.1μg.g-1, with median and average values of 10.7 and 11.2μg.g-1 and a coefficient of variation of 32%.  Whilst minimum, median and average values were very similar to those reported in 2006 and 2008 (Table 5.11), the maximum value and the coefficient of variation were substantially higher than in those surveys.

Figure 5.9 indicates that, over most of the survey area, there has been a reduction in mercury concentration, with the maximum value isolated at station 3, and a substantial reduction in particular at station 14, 18, 19 and 21.  Although the coefficient of variation is higher than previously, this is largely due to an increase in the number of stations with low concentrations.

Table 5.11 Summary statistics for lead, 2006-2010

|  | Pb |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 7.4 | 7.5 | 8.3 |
| Max | 15.6 | 13.8 | 32.1 |
| Median | 11.5 | 10.8 | 10.7 |
| Average | 11.8 | 10.8 | 11.2 |
| St Dev | 1.7 | 1.6 | 3.5 |
| CV | 14% | 15% | 32% |

Figure 5.9 Contour plots, average lead concentrations, 2008 and 2010

Zinc

Zinc concentrations ranged from 30.2 to 63.6μg.g-1, with median and average values of 50 and 48.1μg.g-1, and a coefficient of variation of 18%.  The minimum value was lower than in 2008, but higher than in 2006.  The maximum value was substantially lower than in 2008, but similar to that in 2006.  Median and average values were intermediate between the 2006 and 2008 values, and the coefficient of variation was slightly higher than in the two previous surveys.

Figure 5.10 indicates a persistent patch of higher concentration around stations 8 and 12, but substantially lower concentrations at stations 5 and 10 than were previously observed.

Table 5.12 Summary statistics for zinc, 2006-2010

|  | Zn |
| --- | --- |
|  | 2006 | 2008 | 2010 |
| Min | 19.8 | 34.5 | 30.2 |
| Max | 58.9 | 82.1 | 63.6 |
| Median | 46.0 | 56.6 | 50.0 |
| Average | 45.4 | 55.1 | 48.1 |
| St Dev | 6.7 | 8.3 | 8.5 |
| CV | 15% | 15% | 18% |

Figure 5.10 Contour plots, average zinc concentrations, 2008 and 2010

## Relationship between Metals

Table 5.13 presents the results of correlation analysis for all metals measured.  There are two distinct groups within which strong intercorrelations are evident:

- Barium (both extracted forms) and cadmium

- Iron, manganese, chromium, and zinc

A strong intercorrelation between the members of the second group would be expected, as these elements are all relatively abundant in material of geological origin.  Copper and lead concentrations are only weakly positively correlated with the second group of metals, whilst mercury concentrations have a very weak negative relationship with chromium, iron, manganese and zinc concentrations and are unrelated to other metal concentrations.

Barium and cadmium concentrations have either no (Pb, Cu, Hg), or very weak negative (Fe, Mn, Cr, Zn), association with other metals.

Table 5.13	Correlation between Replicate Metal Concentrations, East Azeri Survey 2010

|  | Ba | Ba Fusion | Cd | Cr | Cu | Hg | Fe | Mn | Pb | Zn |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ba | 1.00 |  |  |  |  |  |  |  |  |  |
| Ba Fusion | 0.98 | 1.00 |  |  |  |  |  |  |  |  |
| Cd | 0.94 | 0.92 | 1.00 |  |  |  |  |  |  |  |
| Cr | -0.31 | -0.23 | -0.40 | 1.00 |  |  |  |  |  |  |
| Cu | 0.14 | 0.20 | 0.07 | 0.43 | 1.00 |  |  |  |  |  |
| Hg | 0.06 | 0.02 | 0.12 | -0.32 | 0.22 | 1.00 |  |  |  |  |
| Fe | -0.38 | -0.33 | -0.45 | 0.93 | 0.21 | -0.39 | 1.00 |  |  |  |
| Mn | -0.20 | -0.21 | -0.29 | 0.62 | 0.09 | -0.33 | 0.71 | 1.00 |  |  |
| Pb | 0.21 | 0.23 | 0.10 | 0.12 | 0.43 | 0.32 | 0.06 | 0.04 | 1.00 |  |
| Zn | -0.13 | -0.05 | -0.27 | 0.91 | 0.61 | -0.20 | 0.82 | 0.59 | 0.35 | 1.00 |

As noted earlier in this chapter, the overall variation for most metals was small, with the majority of concentrations of most metals lying within 25% of the relevant median value and thus close to, or within, the limits of sampling and analytical uncertainty.  For most metals, a general reduction in overall concentration is also evident, and concentrations lie within the range established during baseline surveys as representing a natural background for the ACG Contract Area.  Although some contour plots show distinct changes in the distribution of patterns of concentration, these changes have occurred within the window of ‘normal’ conditions, and present no indication of recent contamination.  The changes might, however, indicate the progressive distribution and re-distribution of geological material derived from cuttings; if this is the case, then in most instances there is little evidence that the mineral composition of the cuttings is substantially different from that of the mineral component of natural seabed sediments.

Barium and cadmium are clearly different from other metals, in terms of both the distribution of concentration and of absolute changes in concentration.  It is notable that, although the range of concentration of barium has reduced progressively from 2006 to 2010, the average value for 2010 was slightly higher than in 2008, and the contour plots suggest a progressive spread of barium resulting in lower maximum concentration but a more even distribution over a larger part of the survey area.  In 2006, 2008 and 2010 there was a distinct association between barium and cadmium concentration; however, although concentrations of barium generally reduced between 2008 and 2010, concentrations of cadmium were in 2010 on average more than twice the concentrations reported in 2008.  Figure  5.11 compares the relationship between these two metals for all three surveys.  The most striking feature of this figure is the difference in slope of the regression for the 2010 data compared to both the 2006 and 2008 data; this indicates that in 2010 cadmium concentrations were approximately 3-5 times higher per unit barium concentration than in the two previous surveys; Table 5.5 indicates that this is not just a relative change, but also an absolute increase in concentration of on average a factor of 2.

Figure 5.11  Scatter plot of Ba against Cd for 2006, 2008 and 2010

## Comparison to Previous East Azeri Survey Data

Table 5.14 presents a station-by station comparison of average metal concentrations over four surveys.  To aid the comparison, stations where the 2010 concentrations were higher than in 2008 are highlighted in yellow.  From this, it is clear that the most marked increases are observed for barium and cadmium;  although concentrations were higher at the majority of stations for arsenic, mercury and lead,  the differences for these metals were predominantly small, and within the limits of analytical uncertainty.

Table 5.14 Comparable Metal Concentrations East Azeri Surveys 2006, 2008 and 2010 μg.g-1

|  | As | Ba | Ba fusion | Cd |
| --- | --- | --- | --- | --- |
|  | 2002 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 |
| 1 | 3.6 | 5 | 4.4 | 9.9 | 799 | 2 220 | 3970 | 3279 | 2 675 | 4990 | 4132 | 0.174 | 0.2 | 0.36 | 0.50 |
| 2 | 3.7 | 5.4 | 8.6 | 11.8 | 1166 | 2 155 | 2150 | 2877 | 2 645 | 2950 | 3446 | 0.171 | 0.25 | 0.24 | 0.43 |
| 3 | 6.2 | 7.4 | 7 | 12.7 | 912 | 10 135 | 2650 | 2810 | 11 915 | 3025 | 3774 | 0.162 | 0.53 | 0.27 | 0.28 |
| 4 | 4.7 | 6.2 | 5 | 12.4 | 868 | 15 400 | 4690 | 5276 | 16 685 | 5610 | 6775 | 0.182 | 0.73 | 0.36 | 0.69 |
| 5 | 4.2 | 6.4 | 5.5 | 9.9 | 1067 | 9 390 | 4225 | 5040 | 12 420 | 5015 | 7567 | 0.184 | 0.33 | 0.34 | 0.80 |
| 6 | 3.4 | 10.4 | 11.2 | 11.7 | 2538 | 3 085 | 1600 | 1790 | 3 780 | 1829 | 2627 | 0.17 | 0.33 | 0.27 | 0.36 |
| 7 | 3.6 | 9.3 | 6.7 | 12.1 | 656 | 2 865 | 1511 | 1801 | 3 470 | 1730 | 2480 | 0.155 | 0.34 | 0.23 | 0.33 |
| 8 | 2.7 | 14.6 | 7.2 | 16.6 | 1053 | 8 755 | 4955 | 1998 | 9 910 | 5470 | 2651 | 0.169 | 0.3 | 0.32 | 0.35 |
| 9 |  | 7.2 | 7.3 | 11.9 |  | 5 170 | 2585 | 6700 | 7 200 | 2735 | 9846 |  | 0.31 | 0.29 | 1.16 |
| 10 | 5.4 | 13.5 | 8.9 | 10.4 | 720 | 1 820 | 1680 | 2921 | 2 940 | 1972 | 3674 | 0.151 | 0.23 | 0.27 | 0.55 |
| 11 | 3.2 | 14.2 | 4.3 | 12.6 | 2082 | 5 020 | 1825 | 1755 | 6 195 | 1985 | 2733 | 0.183 | 0.41 | 0.27 | 0.49 |
| 12 | 4.7 | 12.5 | 9.9 | 14.7 | 1055 | 571 | 920 | 2716 | 718 | 1040 | 4147 | 0.144 | 0.14 | 0.19 | 0.50 |
| 13 | 3.6 | 10.5 | 7.3 | 11.0 | 1604 | 5 525 | 7625 | 3787 | 6 625 | 8870 | 5284 | 0.148 | 0.39 | 0.45 | 0.74 |
| 14 | 3 | 9.3 | 7.9 | 10.5 | 1042 | 11 335 | 11450 | 5340 | 16 400 | 14130 | 7815 | 0.151 | 0.47 | 0.53 | 0.93 |
| 15 | 9.5 | 24.9 | 11.9 | 18.8 | 869 | 5 950 | 2522 | 3475 | 8 150 | 3005 | 4639 | 0.182 | 0.23 | 0.27 | 0.70 |
| 16 |  | 14.4 | 7.7 | 12.9 |  | 836 | 792 | 1745 | 1 093 | 900 | 2275 |  | 0.09 | 0.2 | 0.37 |
| 17 |  | 7.6 | 10.4 | 10.3 |  | 642 | 701 | 724 | 1 225 | 820 | 927 |  | 0.14 | 0.2 | 0.14 |
| 18 |  | 5.5 | 5.4 | 8.1 |  | 5 890 | 4515 | 5133 | 6 870 | 5190 | 6410 |  | 0.44 | 0.38 | 0.98 |
| 19 |  | 8.8 | 6.8 | 12.0 |  | 1 390 | 1170 | 1184 | 1 650 | 1235 | 1495 |  | 0.22 | 0.23 | 0.27 |
| 20 |  | 7.5 | 4.8 | 11.6 |  | 870 | 3380 | 2589 | 1 815 | 3860 | 3071 |  | 0.19 | 0.28 | 0.53 |
| 21 |  | 15.1 | 16.7 | 16.4 |  | 5 220 | 1355 | 5000 | 6 990 | 1690 | 6050 |  | 0.2 | 0.21 | 1.05 |

Table 5.14 (Continued) Comparable Metal Concentrations East Azeri Surveys 2006, 2008 and 2010 μg.g-1

|  | Cr | Cu | Fe | Hg |
| --- | --- | --- | --- | --- |
|  | 2002 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 |
| 1 | 49.3 | 48.3 | 41.4 | 38.7 | 29.1 | 35.1 | 34.4 | 27.9 | 21265 | 20 900 | 18400 | 16193 | 0.014 | 0.02 | 0.032 | 0.032 |
| 2 | 43 | 47.5 | 44 | 30.4 | 25.1 | 33.3 | 23.3 | 21.3 | 18710 | 20 250 | 22300 | 15287 | 0.013 | 0.02 | 0.03 | 0.032 |
| 3 | 43.1 | 54.3 | 48.7 | 41.8 | 24.4 | 36.5 | 30.9 | 28.9 | 22261 | 23 950 | 22875 | 18843 | 0.013 | 0.02 | 0.028 | 0.033 |
| 4 | 44.7 | 40.3 | 47.1 | 38.7 | 30.7 | 36.4 | 33 | 28.8 | 20105 | 18 150 | 21300 | 17824 | 0.02 | 0.02 | 0.022 | 0.028 |
| 5 | 40.7 | 43 | 58.4 | 40.6 | 28.9 | 37.9 | 39.2 | 27.8 | 18171 | 19 500 | 27250 | 16992 | 0.02 | 0.02 | 0.025 | 0.026 |
| 6 | 45.4 | 25.7 | 48.3 | 31.3 | 23.2 | 17.5 | 28.9 | 18.7 | 17500 | 14 370 | 23250 | 16326 | 0.025 | 0.01 | 0.047 | 0.026 |
| 7 | 58.4 | 45.2 | 57.5 | 44.3 | 28.2 | 32.1 | 29.5 | 25.0 | 23741 | 21 050 | 26500 | 20680 | 0.016 | 0.02 | 0.032 | 0.024 |
| 8 | 54.9 | 36.9 | 56.8 | 55.0 | 32 | 33 | 26.3 | 22.8 | 20847 | 18 450 | 27650 | 27543 | 0.024 | 0.02 | 0.045 | 0.017 |
| 9 |  | 46.1 | 50 | 42.8 |  | 36 | 36.5 | 29.9 |  | 20 500 | 22500 | 19277 |  | 0.02 | 0.046 | 0.026 |
| 10 | 59.2 | 45.6 | 54.4 | 33.1 | 23.1 | 28 | 27.3 | 20.4 | 25656 | 27 200 | 26750 | 15902 | 0.018 | 0.02 | 0.046 | 0.027 |
| 11 | 39.4 | 31.5 | 45.2 | 39.9 | 23.7 | 23.5 | 27.3 | 32.1 | 17800 | 16 600 | 19250 | 17729 | 0.014 | 0.01 | 0.022 | 0.027 |
| 12 | 42.6 | 55.1 | 59.1 | 51.6 | 25.1 | 30.6 | 27.8 | 26.9 | 20320 | 30 200 | 29150 | 24204 | 0.024 | 0.02 | 0.022 | 0.020 |
| 13 | 40.8 | 36.3 | 46.7 | 37.8 | 21.7 | 34.9 | 27.5 | 21.3 | 16706 | 17 850 | 21950 | 16253 | 0.018 | 0.02 | 0.025 | 0.020 |
| 14 | 42.3 | 47.8 | 42.6 | 41.8 | 25.3 | 31 | 27.3 | 23.8 | 17426 | 21 950 | 19550 | 18556 | 0.024 | 0.03 | 0.028 | 0.034 |
| 15 | 58.5 | 44.7 | 51.5 | 42.1 | 26 | 34.2 | 28.4 | 25.3 | 27960 | 29 250 | 25800 | 20762 | 0.018 | 0.03 | 0.024 | 0.024 |
| 16 |  | 49.5 | 55.5 | 41.9 |  | 35.2 | 34.6 | 25.0 |  | 22 350 | 25200 | 18061 |  | 0.02 | 0.02 | 0.044 |
| 17 |  | 43.3 | 55.1 | 44.6 |  | 27.3 | 25.8 | 21.2 |  | 21 350 | 25450 | 20362 |  | 0.02 | 0.018 | 0.030 |
| 18 |  | 34 | 35.5 | 28.1 |  | 36.4 | 30.7 | 24.6 |  | 17 250 | 17550 | 12329 |  | 0.02 | 0.024 | 0.037 |
| 19 |  | 38.8 | 47.8 | 42.0 |  | 29.4 | 28.8 | 24.1 |  | 19 100 | 22900 | 20202 |  | 0.02 | 0.023 | 0.036 |
| 20 |  | 44 | 39.4 | 44.0 |  | 28.4 | 33.5 | 28.2 |  | 21 350 | 18550 | 21370 |  | 0.02 | 0.027 | 0.045 |
| 21 |  | 34.8 | 57.1 | 27.2 |  | 37.2 | 31.3 | 15.4 |  | 19 850 | 28700 | 14528 |  | 0.11 | 0.036 | 0.030 |

Table 5.14 (Continued) Comparable Metal Concentrations East Azeri Surveys 2006, 2008 and 2010 μg.g-1

|  | Mn | Pb | Zn |
| --- | --- | --- | --- |
|  | 2002 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 | 2002 | 2006 | 2008 | 2010 |
| 1 | 402 | 428 | 404 | 333 | 24.5 | 11.7 | 11.9 | 11.3 | 48.4 | 50.9 | 51.9 | 50.1 |
| 2 | 344 | 408 | 361 | 452 | 27.3 | 11.4 | 10.8 | 11.0 | 42.7 | 45.9 | 48.5 | 42.7 |
| 3 | 419 | 576 | 487 | 414 | 14.9 | 13.8 | 11.6 | 21.2 | 47.1 | 54.3 | 54.7 | 55.1 |
| 4 | 363 | 369 | 453 | 336 | 21.9 | 13.5 | 10.8 | 11.6 | 45.9 | 43.4 | 54 | 49.1 |
| 5 | 331 | 360 | 532 | 356 | 21.7 | 13.3 | 12.1 | 10.7 | 43.3 | 46.4 | 65.4 | 49.6 |
| 6 | 351 | 360 | 434 | 324 | 25.9 | 8.4 | 10.8 | 9.1 | 39.9 | 31.3 | 49.7 | 38.9 |
| 7 | 490 | 615 | 554 | 445 | 18.7 | 11.6 | 9.3 | 10.1 | 52.6 | 45.8 | 58.5 | 50.5 |
| 8 | 409 | 558 | 520 | 512 | 16.5 | 12.7 | 11.1 | 11.5 | 48.5 | 44.8 | 60.7 | 61.8 |
| 9 |  | 415 | 413 | 383 |  | 11.8 | 10.2 | 12.6 |  | 51.1 | 54.8 | 58.4 |
| 10 | 458 | 490 | 489 | 316 | 21.1 | 11.5 | 11.3 | 10.0 | 49.4 | 48.3 | 67 | 41.4 |
| 11 | 328 | 573 | 422 | 317 | 23.4 | 10.1 | 8.2 | 10.9 | 37.6 | 51.2 | 49.2 | 46.4 |
| 12 | 419 | 520 | 540 | 442 | 31.5 | 11.6 | 10.4 | 11.3 | 42.6 | 50.9 | 59.8 | 56.6 |
| 13 | 422 | 415 | 434 | 323 | 28.7 | 12.2 | 11.3 | 10.2 | 38.2 | 42.9 | 60.7 | 44.4 |
| 14 | 388 | 467 | 389 | 368 | 23.2 | 14 | 13.7 | 12.2 | 39.7 | 48.1 | 52.3 | 50.3 |
| 15 | 552 | 505 | 491 | 407 | 27.2 | 15.3 | 11.3 | 12.6 | 60.7 | 46.8 | 57.5 | 50.3 |
| 16 |  | 443 | 482 | 351 |  | 10.8 | 10.6 | 10.0 |  | 46.5 | 58.3 | 46.9 |
| 17 |  | 433 | 469 | 389 |  | 10.4 | 9.4 | 9.5 |  | 43.2 | 56 | 49.8 |
| 18 |  | 387 | 385 | 306 |  | 12.1 | 11.7 | 10.1 |  | 35.8 | 42.3 | 36.1 |
| 19 |  | 395 | 447 | 388 |  | 10.4 | 10.1 | 10.5 |  | 43.7 | 52.6 | 50.0 |
| 20 |  | 402 | 538 | 376 |  | 10.4 | 8.7 | 10.9 |  | 44.1 | 46.7 | 50.7 |
| 21 |  | 919 | 595 | 378 |  | 11.2 | 10.5 | 8.7 |  | 37.9 | 55.8 | 31.1 |

## Metal Summary

Overall, there was little real change in concentration for the majority of metals, with either a minor decrease or increase except in the case of barium and cadmium.  With the exception of these two metals, spatial variation was limited, concentrations remained within the contract area baseline range, and, although it is not possible to determine the relative contribution of cuttings and natural sediment, there is no observable indication of contamination.

Both barium and cadmium exhibit a more distinctive pattern,  with a clear ‘footprint’ to the east of the platform, and increases in concentration at the majority of stations.  In the case of barium, the increases are moderate, and, in combination with a decrease in maximum concentrations, may represent a general spreading of cuttings and consequent homogenisation of sediments.  In the case of cadmium, two points can be noted:

- as in previous EA surveys (and many other ACG area surveys) there is a strong association with barium

- although the association between cadmium and barium is persistent, the statistical characteristics of the relationship have changed since 2008;  concentrations of cadmium are considerably higher than in previous surveys, and the slope of the regression relating concentrations of the two metals is 3-5 times steeper than in previous surveys.

The data do not permit a firm explanation of these changes within the context of this survey alone. In principle, the differences might be accounted for by relatively recent discharge and dispersion of cuttings with substantially higher cadmium concentrations than were present in pre-2008 discharges.  This could, perhaps, be confirmed by obtaining core samples from the cuttings piles, and determining cadmium concentrations down a series of depth horizons.  It is also possible that cadmium levels in barite used since 2008 are higher than in barite used prior to 2008, although it is understood that the mud supplier applies the EPA limits which are reflected in the PSA and in subsequent ESIAs.  Neither possibility can be evaluated without

- additional information on the chemistry of drilling mud and cuttings and

- an overall review of 2010 data, to establish whether the phenomena associated with cadmium are directly related to local conditions, or whether they are due to analytical interferences which are not fully controlled by the established and approved analytical and QA/QC methodologies